Fireball International - 2013 Technical Committee Report

Day-to-Day Business

As usual, there have been rule interpretation questions from NCAs, sail makers, boat builders and individuals.  Most of these questions were forwarded to the Technical Committee by the Class Secretary, but a significant number were raised on the various websites, and some were addressed directly to the Technical Committee Chairman.

Examples of questions brought up since the last World Championships include:

- The legality of carbon countdown watch mounts (Robin Inns, AUS);

- Recommended tolerances for wood boat builders (Dave White, USA);

- The use of “soft” rigging (Peter Kelly, CAN); and

- The legality of “string” sails (lots and lots of people, UK).

Rule Changes

Since the last World Championships, Rule IFCR 9.1.5 was changed to reduce the depth of the gunwhale rubbers from 15 mm to 10 mm.  This was done to give boat builders the option of using a roll-over type of construction to mate the hull shell to the deck shell.

Rule Change Proposals

The following rule change proposals will be forth for voting this fall:

- Defining additional sail reinforcement dimensions (e.g. batten pocket outer dimensions, tabling widths…);

- Allowing a mainsail flattening reef point;

- Updating the spinnaker measurements to be fully compliant with ISAF terminology; and

- Allowing sail makers to undertake in-house certifications;

Development

A review of the measurement methods for the jibs is still underway as the current method set out by ISAF doesn’t really work. ISAF is looking into whether their jib measurement methods can be modified to improve the repeatability of measurement, but it might be required to introduce additional measurement points in the jib over and above the ISAF requirements.

The identification of NCA-nominated measurers is still a problem. Basically, FI does not know who these measurers are, and it makes sail measurement and compliance very difficult at international championships.  A database of measurers and signatures is needed to make sure things go smoothly at future championships.  Various options, including FI-supplied measurement stamps; sail buttons; Web-based sail registration; and in-house certification by the sail makers are all options that are being considered.

Phil Locker (CAN) has been given permission to trial composite booms.

The technical committee has been working on the design of a steel shipping rack that would allow for the transport of ten boats (eight on their trolleys) in a high-cube 40’ container.  This approach would make it easier, and much quicker, to pack and unpack containers.

Respectfully submitted,

Thomas Egli, Fireball International Technical Committee Chairman